## Slide 1: CSE 311: Foundations of Computing
Lecture 3: Digital Circuits

## Slide 2: Review: Propositional Logic
Propositions
  atomic propositions are T/F-valued variables
  combined using logical connectives (not, and, or, etc.)
  can be described by a truth table
    shows the truth value of the proposition in
    each combination of truth values of the atomic propositions
Logical equivalence
  used to simplify logical expressions
First application
  Simplifying English sentences
p | q | p  q
T | T | T
T | F | F
F | T | F
F | F | F

## Slide 3: Truth Table to show tautology
(p  r)  (r  p)
T | T | T | T | T
T | F | F | T | T
F | T | F | T | T
F | F | F | F | T
T | T | T | T | T
T | F | F | T | T
F | T | F | T | T
F | F | F | F | T
T

## Slide 4: Logical Proofs of Equivalence
(p  r)  (r  p)
Use a series of equivalences like so:
T
Law of Implication
De Morgan
Associative
Associative
Commutative
Associative
Commutative (twice)
Negation (twice)
Domination/Identity

## Slide 5: Logical Proofs of Equivalence/Tautology
Not smaller than truth tables when there are only a few propositional variables...
...but usually much shorter than truth table proofs when there are many propositional variables
A big advantage will be that we can extend them to a more in-depth understanding of logic for which truth tables don’t apply.

## Slide 6: Another key application: Digital Circuits
Computing With Logic
  T corresponds to 1 or “high” voltage
  F corresponds to 0 or “low” voltage
Gates
  Take inputs and produce outputs (functions)
  Several kinds of gates
  Correspond to propositional connectives (most of them)

## Slide 7: Circuits: AND, OR, NOT Gates
p | q | p  q
T | T | T
T | F | F
F | T | F
F | F | F
p | q | OUT
1 | 1 | 1
1 | 0 | 0
0 | 1 | 0
0 | 0 | 0
AND Gate
p
OUT
AND
q
OR Gate
p | q | OUT
1 | 1 | 1
1 | 0 | 1
0 | 1 | 1
0 | 0 | 0
p
OUT
OR
q
p | q | p  q
T | T | T
T | F | T
F | T | T
F | F | F
NOT Gate
p | OUT
1 | 0
0 | 1
p
OUT
NOT
p |  p
T | F
F | T

## Slide 8: Combinational Logic Circuits
Values get sent along wires connecting gates
NOT
OR
AND
AND
NOT
p
q
r
s
OUT

## Slide 9: Combinational Logic Circuits
Values get sent along wires connecting gates
NOT
OR
AND
AND
NOT
p
q
r
s
OUT

## Slide 10: Combinational Logic Circuits
Wires can send one value to multiple gates!
OR
AND
NOT
AND
p
q
r
OUT

## Slide 11: Combinational Logic Circuits
Wires can send one value to multiple gates!
OR
AND
NOT
AND
p
q
r
OUT

## Slide 12: Other Useful Gates
NAND
NOR
XOR
XNOR
p
q
out
p q out 0 0 1 0 1 1 1 0 1
1 1 0
p q out 0 0 1 0 1 0 1 0 0
1 1 0
out
p
q
p
q
out
p q out
0 0 1 0 1 0 1 0 0
1 1 1
p q out 0 0 0 0 1 1 1 0 1
1 1 0
out
p
q

## Slide 13: Boolean Logic
Combinational Logic
  output = F(input)
Sequential Logic
  outputt = F(outputt-1, inputt)
    output dependent on history
    concept of a time step (clock, t)
  Covered in CSE 369

## Slide 14: Boolean Logic
Combinational Logic
  output = F(input)
Boolean Algebra: another notation for logic consisting of…
  a set of elements B = {0, 1}
  binary operations { + , • } (OR, AND)
  and a unary operation { ’ } (NOT )

## Slide 15: Boolean Algebra
Usual notation used in circuit design
Boolean algebra
  a set of elements B containing {0, 1}
  binary operations { + , • }
  and a unary operation { ’ }
  such that the following axioms hold:
For any a, b, c in B: 1. closure: a + b is in B a • b is in B 2. commutativity: a + b = b + a a • b = b • a 3. associativity: a + (b + c) = (a + b) + c a • (b • c) = (a • b) • c 4. distributivity: a + (b • c) = (a + b) • (a + c) a • (b + c) = (a • b) + (a • c) 5. identity: a + 0 = a a • 1 = a 6. complementarity: a + a’ = 1 a • a’ = 0
7. null: a + 1 = 1 a • 0 = 0
8. idempotency: a + a = a a • a = a
9. involution: (a’)’ = a

## Slide 16: Proving Theorems
Using truth table:
(X + Y)’ = X’ • Y’ NOR is equivalent to AND with inputs complemented
(X • Y)’ = X’ + Y’ NAND is equivalent to OR with inputs complemented
X Y X’ Y’ (X + Y)’ X’ • Y’
X Y X’ Y’ (X • Y)’ X’ + Y’
0 0 1 1 1 1
0 1 1 0 1 1 1 0 0 1 1 1
1 1 0 0 0 0
0 0 1 1 1 1
0 1 1 0 0 0
1 0 0 1 0 0
1 1 0 0 0 0
  For example, de Morgan’s Law:
More generally

## Slide 17: Proving Theorems
Using the laws of Boolean Algebra:
  prove the “Uniting theorem”: X • Y + X • Y’ = X prove the “Absorption theorem”: X + X • Y = X
X • Y + X • Y’ =
X + X • Y =

## Slide 18: Proving Theorems
Using the laws of Boolean Algebra:
  prove the “Uniting theorem”: X • Y + X • Y’ = X prove the “Absorption theorem”: X + X • Y = X
distributivity
complementarity
identity
identity
distributivity
commutativity
null
identity
X • Y + X • Y’ = X • (Y + Y’)
= X • 1
= X
X + X • Y = X • 1 + X • Y
= X • (1 + Y)
= X • (Y + 1)
= X • 1
= X

## Slide 19: A Combinational Logic Example
Sessions of Class:
We would like to compute the number of lectures or quiz sections remaining at the start of a given day of the week.
  Inputs: Day of the Week, Lecture/Section flag
  Output: Number of sessions left
  Examples: Input: (Wednesday, Lecture) Output: 2
  Input: (Monday, Section) Output: 1

## Slide 20: Implementation in Software
public int classesLeftInMorning(int weekday, boolean isLecture) {
switch (weekday) {
case SUNDAY:
case MONDAY:
return isLecture ? 3 : 1;
case TUESDAY:
case WEDNESDAY:
return isLecture ? 2 : 1;
case THURSDAY:
return isLecture ? 1 : 1;
case FRIDAY:
return isLecture ? 1 : 0;
case SATURDAY:
return isLecture ? 0 : 0;
}
}

## Slide 21: Implementation with Combinational Logic
Encoding:
  How many bits for each input/output?
  Binary number for weekday
  One bit for each possible output
isLecture
Weekday
0
1
2
3

## Slide 22: Defining Our Inputs!
Weekday | Number | Binary
Sunday | 0 | (000)2
Monday | 1 | (001)2
Tuesday | 2 | (010)2
Wednesday | 3 | (011)2
Thursday | 4 | (100)2
Friday | 5 | (101)2
Saturday | 6 | (110)2
Weekday Input:
  Binary number for weekday
  Sunday = 0, Monday = 1, …
  We care about these in binary:

## Slide 23: Converting to a Truth Table!
Weekday |  | isLecture | c0 | c1 | c2 | c3
SUN | 000 | 0 |  |  |  | 
SUN | 000 | 1 |  |  |  | 
MON | 001 | 0 |  |  |  | 
MON | 001 | 1 |  |  |  | 
TUE | 010 | 0 |  |  |  | 
TUE | 010 | 1 |  |  |  | 
WED | 011 | 0 |  |  |  | 
WED | 011 | 1 |  |  |  | 
THU | 100 | - |  |  |  | 
FRI | 101 | 0 |  |  |  | 
FRI | 101 | 1 |  |  |  | 
SAT | 110 | - |  |  |  | 
- | 111 | - |  |  |  | 
case SUNDAY or MONDAY:
return isLecture ? 3 : 1;
case TUESDAY or WEDNESDAY:
return isLecture ? 2 : 1;
case THURSDAY:
return isLecture ? 1 : 1;
case FRIDAY:
return isLecture ? 1 : 0;
case SATURDAY:
return isLecture ? 0 : 0;

## Slide 24: Converting to a Truth Table!
Weekday |  | isLecture | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
case SUNDAY or MONDAY:
return isLecture ? 3 : 1;
case TUESDAY or WEDNESDAY:
return isLecture ? 2 : 1;
case THURSDAY:
return isLecture ? 1 : 1;
case FRIDAY:
return isLecture ? 1 : 0;
case SATURDAY:
return isLecture ? 0 : 0;

## Slide 25: Truth Table to Logic (Part 1)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
Let’s begin by finding an expression for c3. To do this, we look at the rows where c3 = 1 (true).

## Slide 26: Truth Table to Logic (Part 1)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
DAY == SUN && L == 1
DAY == MON && L == 1

## Slide 27: Truth Table to Logic (Part 1)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
d2d1d0 == 000 && L == 1
d2d1d0 == 001 && L == 1
Substituting DAY for the binary representation.

## Slide 28: Truth Table to Logic (Part 1)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
d2 == 0 && d1 == 0 && d0 == 0 && L == 1
d2 == 0 && d1 == 0 && d0 == 1 && L == 1
Splitting up the bits of the day; so, we can write a formula.

## Slide 29: Truth Table to Logic (Part 1)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
d2’•d1’•d0’•L
d2’•d1’•d0•L
Replacing with Boolean Algebra…

## Slide 30: Truth Table to Logic (Part 1)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
d2’•d1’•d0’•L
d2’•d1’•d0•L
How do we combine them?

## Slide 31: Truth Table to Logic (Part 1)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
d2’•d1’•d0’•L
d2’•d1’•d0•L
Either situation causes c3 to be true. So, we “or” them.
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L

## Slide 32: Truth Table to Logic (Part 2)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
Now, we do c2.
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L

## Slide 33: Truth Table to Logic (Part 3)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
Now, we do c1:
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L
c2 = d2’•d1•d0’•L + d2’•d1•d0•L

## Slide 34: Truth Table to Logic (Part 3)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
Now, we do c1:
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L
d2’•d1’•d0’•L’
d2’•d1’•d0•L’
c2 = d2’•d1•d0’•L + d2’•d1•d0•L
d2’•d1•d0’•L’
d2’•d1•d0•L’
d2•d1’•d0•L
???

## Slide 35: Truth Table to Logic (Part 3)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
Now, we do c1:
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L
d2’•d1’•d0’•L’
d2’•d1’•d0•L’
c2 = d2’•d1•d0’•L + d2’•d1•d0•L
d2’•d1•d0’•L’
d2’•d1•d0•L’
d2•d1’•d0•L
d2•d1’•d0’
No matter what L is, we always say it’s 1. So, we don’t need L in the expression.

## Slide 36: Truth Table to Logic (Part 3)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
Now, we do c1:
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L
d2’•d1’•d0’•L’
d2’•d1’•d0•L’
c2 = d2’•d1•d0’•L + d2’•d1•d0•L
d2’•d1•d0’•L’
d2’•d1•d0•L’
d2•d1’•d0•L
d2•d1’•d0’
No matter what L is, we always say it’s 1. So, we don’t need L in the expression.
c1 = d2’•d1’•d0’•L’ + d2’•d1’•d0•L’ + d2’•d1•d0’•L’ + d2’•d1•d0•L’ + d2•d1’•d0’ + d2•d1’•d0•L

## Slide 37: Truth Table to Logic (Part 4)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
Finally, we do c0:
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L
c2 = d2’•d1•d0’•L + d2’•d1•d0•L
d2•d1’•d0•L’
d2•d1•d0
d2•d1•d0’
c1 = d2’•d1’•d0’•L’ + d2’•d1’•d0•L’ +
d2’•d1•d0’•L’ + d2’•d1•d0•L’ +
d2•d1’•d0’ + d2•d1’•d0•L

## Slide 38: Truth Table to Logic (Part 4)
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L
c2 = d2’•d1•d0’•L + d2’•d1•d0•L
c1 = d2’•d1’•d0’•L’ + d2’•d1’•d0•L’ + d2’•d1•d0’•L’ + d2’•d1•d0•L’ + d2•d1’•d0’ + d2•d1’•d0•L
c0 = d2•d1’•d0•L’ + d2•d1•d0’ + d2•d1•d0
d2
d1
d0
L
NOT
NOT
NOT
OR
AND
AND
Here’s c3 as a circuit:

## Slide 39: Simplifying using Boolean Algebra
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L
= d2’•d1’•(d0’ + d0)•L
= d2’•d1’•1•L
= d2’•d1’•L
AND
d2
d1
L
NOT
NOT

## Slide 40
uniting: 10. a • b + a • b’ = a 10D. (a + b) • (a + b’) = a
absorption: 11. a + a • b = a 11D. a • (a + b) = a 12. (a + b’) • b = a • b 12D. (a • b’) + b = a + b
factoring: 13. (a + b) • (a’ + c) = 13D. a • b + a’ • c = a • c + a’ • b (a + c) • (a’ + b)
consensus: 14. (a • b) + (b • c) + (a’ • c) = 14D. (a + b) • (b + c) • (a’ + c) = a • b + a’ • c (a + b) • (a’ + c)
de Morgan’s: 15. (a + b + ...)’ = a’ • b’ • ... 15D. (a • b • ...)’ = a’ + b’ + ...
Simplification using Boolean Algebra