## Slide 1: CSE 311: Foundations of Computing
Lecture 5: DNF, CNF and Predicate Logic

## Slide 2: Warm-up Exercise
Create a Boolean Algebra expression for below in terms of the variables and
1 | 1 | 0
1 | 0 | 1
0 | 1 | 1
0 | 0 | 0
1 | 1 | 0
1 | 0 | 1
0 | 1 | 1
0 | 0 | 0

## Slide 3: Warm-up Exercise
Create a Boolean Algebra expression for “” below in terms of the variables and
Draw this as a circuit (using AND, OR, NOT)

## Slide 4: Combinational Logic Example
Weekday |  | isLecture | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
case SUNDAY or MONDAY:
return isLecture ? 3 : 1;
case TUESDAY or WEDNESDAY:
return isLecture ? 2 : 1;
case THURSDAY:
return isLecture ? 1 : 1;
case FRIDAY:
return isLecture ? 1 : 0;
case SATURDAY:
return isLecture ? 0 : 0;

## Slide 5: Truth Table to Logic (Part 3)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
Now, we do c1:
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L
c2 = d2’•d1•d0’•L + d2’•d1•d0•L

## Slide 6: Truth Table to Logic (Part 3)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
Now, we do c1:
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L
d2’•d1’•d0’•L’
d2’•d1’•d0•L’
c2 = d2’•d1•d0’•L + d2’•d1•d0•L
d2’•d1•d0’•L’
d2’•d1•d0•L’
d2•d1’•d0•L
???

## Slide 7: Truth Table to Logic (Part 3)
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
Now, we do c1:
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L
d2’•d1’•d0’•L’
d2’•d1’•d0•L’
c2 = d2’•d1•d0’•L + d2’•d1•d0•L
d2’•d1•d0’•L’
d2’•d1•d0•L’
d2•d1’•d0•L
d2•d1’•d0’
No matter what L is, we always say it’s 1. So, we don’t need L in the expression.

## Slide 8: Truth Table to Logic (Part 4)
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L
c2 = d2’•d1•d0’•L + d2’•d1•d0•L
c1 = d2’•d1’•d0’•L’ + d2’•d1’•d0•L’ + d2’•d1•d0’•L’ + d2’•d1•d0•L’ + d2•d1’•d0’ + d2•d1’•d0•L
c0 = d2•d1’•d0•L’ + d2•d1•d0’ + d2•d1•d0
d2
d1
d0
L
NOT
NOT
NOT
OR
AND
AND
Here’s c3 as a circuit:
Notes: This procedure shows that {NOT, AND, OR} are universal

## Slide 9: Important Corollaries of this Construction
, ,  can implement any Boolean function
    we didn’t need any others to do this
Actually, just ,  (or , ) are enough
    follows by De Morgan’s laws
Actually, just NAND (or NOR)
Prime(65353)

## Slide 10: Boolean Algebra
Usual notation used in circuit design
Boolean algebra
  a set of elements B containing {0, 1}
  binary operations { + , • }
  and a unary operation { ’ }
  such that the following axioms hold:
For any a, b, c in B: 1. closure: a + b is in B a • b is in B 2. commutativity: a + b = b + a a • b = b • a 3. associativity: a + (b + c) = (a + b) + c a • (b • c) = (a • b) • c 4. distributivity: a + (b • c) = (a + b) • (a + c) a • (b + c) = (a • b) + (a • c) 5. identity: a + 0 = a a • 1 = a 6. complementarity: a + a’ = 1 a • a’ = 0
7. null: a + 1 = 1 a • 0 = 0
8. idempotency: a + a = a a • a = a
9. involution: (a’)’ = a

## Slide 11
uniting: 10. a • b + a • b’ = a 10D. (a + b) • (a + b’) = a
absorption: 11. a + a • b = a 11D. a • (a + b) = a 12. (a + b’) • b = a • b 12D. (a • b’) + b = a + b
factoring: 13. (a + b) • (a’ + c) = 13D. a • b + a’ • c = a • c + a’ • b (a + c) • (a’ + b)
consensus: 14. (a • b) + (b • c) + (a’ • c) = 14D. (a + b) • (b + c) • (a’ + c) = a • b + a’ • c (a + b) • (a’ + c)
de Morgan’s: 15. (a + b + ...)’ = a’ • b’ • ... 15D. (a • b • ...)’ = a’ + b’ + ...
Simplification using Boolean Algebra

## Slide 12: Simplifying using Boolean Algebra
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L
= d2’•d1’•(d0’ + d0)•L
= d2’•d1’•1•L
= d2’•d1’•L
AND
d2
d1
L
NOT
NOT

## Slide 13: 1-bit Binary Adder
A
+ B
S
(COUT)
0 + 0 = 0 (with COUT = 0)
0 + 1 = 1 (with COUT = 0)
1 + 0 = 1 (with COUT = 0)
1 + 1 = 0 (with COUT = 1)

## Slide 14: 1-bit Binary Adder
A
+ B
S
(COUT)
0 + 0 = 0 (with COUT = 0)
0 + 1 = 1 (with COUT = 0)
1 + 0 = 1 (with COUT = 0)
1 + 1 = 0 (with COUT = 1)
Idea: chain these together to add larger numbers
2 4 8
+ 3 7 5
Recall from elementary school:

## Slide 15: 1-bit Binary Adder
A
+ B
S
(COUT)
0 + 0 = 0 (with COUT = 0)
0 + 1 = 1 (with COUT = 0)
1 + 0 = 1 (with COUT = 0)
1 + 1 = 0 (with COUT = 1)
Idea: These are chained together with a carry-in
A A A A A
B B B B B
S S S S S
CIN
COUT
(CIN)
A
+ B
S
(COUT)
0 1 1 1 0
0 1 1 0 1
1 1 0 1 1
CIN
COUT
1 1 0 0

## Slide 16: 1-bit Binary Adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A
B
CIN
COUT
S
A A A A A
B B B B B
S S S S S
CIN
COUT
A | B | CIN | COUT | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 17: 1-bit Binary Adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A A A A A
B B B B B
S S S S S
CIN
COUT
A | B | CIN | COUT | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
A’•B’•CIN
A’•B•CIN’
A•B’•CIN’
A•B•CIN
S = A’•B’•CIN + A’•B•CIN’ +
A•B’•CIN’ + A•B•CIN
Derive an expression for S

## Slide 18: 1-bit Binary Adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A A A A A
B B B B B
S S S S S
CIN
COUT
A•B’•CIN
A•B•CIN’
A’•B•CIN
A•B•CIN
A | B | CIN | COUT | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
S = A’•B’•CIN + A’•B•CIN’ + A•B’•CIN’ + A•B•CIN
COUT = A’•B•CIN + A•B’•CIN +
A•B•CIN’ + A•B•CIN
Derive an expression for COUT

## Slide 19: 1-bit Binary Adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A A A A A
B B B B B
S S S S S
CIN
COUT
COUT = A’•B•CIN + A•B’•CIN + A•B•CIN’ + A•B•CIN
A | B | CIN | COUT | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
S = A’•B’•CIN + A’•B•CIN’ + A•B’•CIN’ + A•B•CIN

## Slide 20: Apply Theorems to Simplify Expressions
The theorems of Boolean algebra can simplify expressions
  e.g., full adder’s carry-out function
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
= A’ B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= A’ B Cin + A B Cin + A B’ Cin + A B Cin’ + A B Cin
= (A’ + A) B Cin + A B’ Cin + A B Cin’ + A B Cin
= (1) B Cin + A B’ Cin + A B Cin’ + A B Cin
= B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= B Cin + A B’ Cin + A B Cin + A B Cin’ + A B Cin
= B Cin + A (B’ + B) Cin + A B Cin’ + A B Cin
= B Cin + A (1) Cin + A B Cin’ + A B Cin
= B Cin + A Cin + A B (Cin’ + Cin)
= B Cin + A Cin + A B (1)
= B Cin + A Cin + A B

## Slide 21: Apply Theorems to Simplify Expressions
The theorems of Boolean algebra can simplify expressions
  e.g., full adder’s carry-out function
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
= A’ B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= A’ B Cin + A B Cin + A B’ Cin + A B Cin’ + A B Cin
= (A’ + A) B Cin + A B’ Cin + A B Cin’ + A B Cin
= (1) B Cin + A B’ Cin + A B Cin’ + A B Cin
= B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= B Cin + A B’ Cin + A B Cin + A B Cin’ + A B Cin
= B Cin + A (B’ + B) Cin + A B Cin’ + A B Cin
= B Cin + A (1) Cin + A B Cin’ + A B Cin
= B Cin + A Cin + A B (Cin’ + Cin)
= B Cin + A Cin + A B (1)
= B Cin + A Cin + A B
adding extra terms creates new factoring opportunities

## Slide 22: A 2-bit Ripple-Carry Adder
A
Sum
Cout
Cin
B
1-Bit Adder
A0
B0
Cout
Cin
Sum0
0
A1
B1
Sum1
Cout
Cin
A2
B2
Sum2
Cout
Cin
Uses the fact that Sum = A’•B’•CIN + A’•B•CIN’ + A•B’•CIN’ + A•B•CIN
is equivalent to Sum = (A ⊕ B) ⊕ CIN

## Slide 23: Mapping Truth Tables to Logic Gates
Given a truth table:
  Write the output in a table
  Write the Boolean expression
  Minimize the Boolean expression
  Draw as gates
  Map to available gates
A B C F
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 0
1 1 1 1
F = A’BC’+A’BC+AB’C+ABC
= A’B(C’+C)+AC(B’+B)
= A’B+AC
2
3
4
5

## Slide 24: Canonical Forms
Truth table is the unique signature of a 0/1 function
The same truth table can have many gate realizations
  We’ve seen this already
  Depends on how good we are at Boolean simplification
Canonical forms
  Standard forms for a Boolean expression
  We all produce the same expression

## Slide 25: Sum-of-Products Canonical Form
AKA Disjunctive Normal Form (DNF)
AKA Minterm Expansion
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
001
011
101
110
111
A’B’C
A’BC
AB’C
ABC’
ABC
F
F= A’B’C + A’BC + AB’C + ABC’ + ABC’
Read T rows off
truth table
Convert to
Boolean Algebra
Add the minterms together
1
2
3

## Slide 26: Sum-of-Products Canonical Form
Product term (or minterm)
  ANDed product of literals – input combination for which output is true
  each variable appears exactly once, true or inverted (but not both)
A B C minterms 0 0 0 A’B’C’
0 0 1 A’B’C
0 1 0 A’BC’
0 1 1 A’BC
1 0 0 AB’C’
1 0 1 AB’C
1 1 0 ABC’
1 1 1 ABC
F in canonical form: F(A, B, C) = A’B’C + A’BC + AB’C + ABC’ + ABC
canonical form  minimal form F(A, B, C) = A’B’C + A’BC + AB’C + ABC + ABC’
      = (A’B’ + A’B + AB’ + AB)C + ABC’
      = ((A’ + A)(B’ + B))C + ABC’ = C + ABC’ = ABC’ + C
= AB + C

## Slide 27: Product-of-Sums Canonical Form
AKA Conjunctive Normal Form (CNF)
AKA Maxterm Expansion
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
F
F =
Read F rows off
truth table
Negate all
bits
Multiply the maxterms together
1
2
4
Convert to
Boolean Algebra
3

## Slide 28: Product-of-Sums Canonical Form
AKA Conjunctive Normal Form (CNF)
AKA Maxterm Expansion
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
000
010
100
F
F = (A + B + C)(A + B’ + C)(A’ + B + C)
111
101
011
A + B + C
A + B’ + C
A’ + B + C
Read F rows off
truth table
Negate all
bits
Multiply the maxterms together
1
2
4
Convert to
Boolean Algebra
3

## Slide 29: Product-of-Sums: Why does this procedure work?
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Useful Facts:
We know (F’)’ = F
We know how to get a minterm expansion for F’
F’ = A’B’C’ + A’BC’ + AB’C’

## Slide 30: Product-of-Sums: Why does this procedure work?
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Useful Facts:
We know (F’)’ = F
We know how to get a minterm expansion for F’
F’ = A’B’C’ + A’BC’ + AB’C’
Taking the complement of both sides…
(F’)’ = (A’B’C’ + A’BC’ + AB’C’)’
And using DeMorgan/Comp.…
F = (A’B’C’)’ (A’BC’)’ (AB’C’)’
F = (A + B + C)(A + B’ + C)(A’ + B + C)

## Slide 31: Product-of-Sums Canonical Form
Sum term (or maxterm)
  ORed sum of literals – input combination for which output is false
  each variable appears exactly once, true or inverted (but not both)
A B C maxterms 0 0 0 A+B+C
0 0 1 A+B+C’
0 1 0 A+B’+C
0 1 1 A+B’+C’
1 0 0 A’+B+C
1 0 1 A’+B+C’
1 1 0 A’+B’+C
1 1 1 A’+B’+C’
F in canonical form: F(A, B, C) = (A + B + C) (A + B’ + C) (A’ + B + C)
canonical form  minimal form F(A, B, C) = (A + B + C) (A + B’ + C) (A’ + B + C)
      = (A + B + C) (A + B’ + C)
      (A + B + C) (A’ + B + C)
      = (A + C) (B + C)

## Slide 32: Predicate Logic

## Slide 33: Predicate Logic
Propositional Logic
  “If you take the high road and I take the low road then I’ll arrive in Scotland before you.”
Predicate Logic
  “All positive integers , , and satisfy .”
Prime(65353)

## Slide 34: Predicate Logic
Propositional Logic
  Allows us to analyze complex propositions in terms of their simpler constituent parts (a.k.a. atomic propositions) joined by connectives
Predicate Logic
  Lets us analyze them at a deeper level by expressing how those propositions depend on the objects they are talking about
Prime(65353)

## Slide 35: Predicate Logic
Adds two key notions to propositional logic
  Predicates
  Quantifiers

## Slide 36: Predicates
Predicate
  A function that returns a truth value, e.g.,
Cat(x) ::= “x is a cat”
Prime(x) ::= “x is prime”
HasTaken(x, y) ::= “student x has taken course y”
LessThan(x, y) ::= “x < y”
Sum(x, y, z) ::= “x + y = z”
GreaterThan5(x) ::= “x > 5”
HasNChars(s, n) ::= “string s has length n”
Predicates can have varying numbers of arguments and input types.
Prime(65353)

## Slide 37: Domain of Discourse
For ease of use, we define one “type”/“domain” that we work over. This non-empty set of objects is called the “domain of discourse”.
For each of the following, what might the domain be?
“x is a cat”, “x barks”, “x ruined my couch”
“x is prime”, “x = 0”, “x < 0”, “x is a power of two”
(3) “student x has taken course y” “x is a pre-req for z”
Relate  and  to  and 
“mammals” or “sentient beings” or “cats and dogs” or …
“numbers” or “integers” or “integers greater than 5” or …
“students and courses” or “university entities” or …

## Slide 38: Quantifiers
We use quantifiers to talk about collections of objects.
x P(x)
  P(x) is true for every x in the domain
  read as “for all x, P of x”
x P(x)
There is an x in the domain for which P(x) is true
  read as “there exists x, P of x”
Relate  and  to  and 

## Slide 39: Quantifiers
We use quantifiers to talk about collections of objects.
Universal Quantifier (“for all”): x P(x)
  P(x) is true for every x in the domain
  read as “for all x, P of x”
Examples:
x Odd(x)
x LessThan4(x)
Relate  and  to  and 
Are these true?

## Slide 40: Quantifiers
We use quantifiers to talk about collections of objects.
Universal Quantifier (“for all”): x P(x)
  P(x) is true for every x in the domain
  read as “for all x, P of x”
Examples:
x Odd(x)
x LessThan4(x)
Relate  and  to  and 
Are these true? It depends on the domain. For example:
{1, 3, -1, -27} | Integers | Odd Integers
True | False | True
True | False | False

## Slide 41: Quantifiers
We use quantifiers to talk about collections of objects.
Existential Quantifier (“exists”): x P(x)
There is an x in the domain for which P(x) is true
  read as “there exists x, P of x”
Examples:
x Odd(x)
x LessThan4(x)
Relate  and  to  and 

## Slide 42: Quantifiers
We use quantifiers to talk about collections of objects.
Existential Quantifier (“exists”): x P(x)
There is an x in the domain for which P(x) is true
  read as “there exists x, P of x”
Examples:
x Odd(x)
x LessThan4(x)
Relate  and  to  and 
Are these true? It depends on the domain. For example:
{1, 3, -1, -27} | Integers | Positive Multiples of 5
True | True | True
True | True | False