## Slide 1: CSE 311: Foundations of Computing
Lecture 4: Boolean Algebra, Circuits, Canonical Forms

## Slide 2: Last Time: Boolean Algebra
Usual notation used in circuit design
Boolean algebra
  a set of elements B containing {0, 1}
  binary operations { + , • }
  and a unary operation { ’ }
  such that the following axioms hold:
For any a, b, c in B: 1. closure: a + b is in B a • b is in B 2. commutativity: a + b = b + a a • b = b • a 3. associativity: a + (b + c) = (a + b) + c a • (b • c) = (a • b) • c 4. distributivity: a + (b • c) = (a + b) • (a + c) a • (b + c) = (a • b) + (a • c) 5. identity: a + 0 = a a • 1 = a 6. complementarity: a + a’ = 1 a • a’ = 0
7. null: a + 1 = 1 a • 0 = 0
8. idempotency: a + a = a a • a = a
9. involution: (a’)’ = a

## Slide 3: Warm-up Exercise
Create a Boolean Algebra expression for below in terms of the variables and
1 | 1 | 0
1 | 0 | 1
0 | 1 | 1
0 | 0 | 0
1 | 1 | 0
1 | 0 | 1
0 | 1 | 1
0 | 0 | 0

## Slide 4: Warm-up Exercise
Create a Boolean Algebra expression for “” below in terms of the variables and
Draw this as a circuit (using AND, OR, NOT)

## Slide 5: Last Time: Combinational Logic
Encoding:
  Binary number for weekday (Binary encoding)
  One bit for each possible output (“1-Hot” encoding)
isLecture
Weekday
0
1
2
3

## Slide 6: Last Time: Truth Table to Logic
 | d2d1d0 | L | c0 | c1 | c2 | c3
SUN | 000 | 0 | 0 | 1 | 0 | 0
SUN | 000 | 1 | 0 | 0 | 0 | 1
MON | 001 | 0 | 0 | 1 | 0 | 0
MON | 001 | 1 | 0 | 0 | 0 | 1
TUE | 010 | 0 | 0 | 1 | 0 | 0
TUE | 010 | 1 | 0 | 0 | 1 | 0
WED | 011 | 0 | 0 | 1 | 0 | 0
WED | 011 | 1 | 0 | 0 | 1 | 0
THU | 100 | - | 0 | 1 | 0 | 0
FRI | 101 | 0 | 1 | 0 | 0 | 0
FRI | 101 | 1 | 0 | 1 | 0 | 0
SAT | 110 | - | 1 | 0 | 0 | 0
- | 111 | - | 1 | 0 | 0 | 0
d2’•d1’•d0’•L
d2’•d1’•d0•L
Either situation causes c3 to be true. So, we “or” them.
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L

## Slide 7: Last Time: Truth Table to Logic
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L
c2 = d2’•d1•d0’•L + d2’•d1•d0•L
c1 = d2’•d1’•d0’•L’ + d2’•d1’•d0•L’ + d2’•d1•d0’•L’ + d2’•d1•d0•L’ + d2•d1’•d0’ + d2•d1’•d0•L
c0 = d2•d1’•d0•L’ + d2•d1•d0’ + d2•d1•d0
d2
d1
d0
L
NOT
NOT
NOT
OR
AND
AND
Here’s c3 as a circuit:

## Slide 8: Simplifying using Boolean Algebra
c3 = d2’•d1’•d0’•L + d2’•d1’•d0•L
= d2’•d1’•(d0’ + d0)•L
= d2’•d1’•1•L
= d2’•d1’•L
AND
d2
d1
L
NOT
NOT

## Slide 9: Important Corollaries of this Construction
, ,  can implement any Boolean function
    we didn’t need any others to do this
Actually, just ,  (or , ) are enough
    follows by De Morgan’s laws
Actually, just NAND (or NOR)
Prime(65353)

## Slide 10: 1-bit Binary Adder
A
+ B
S
(COUT)
0 + 0 = 0 (with COUT = 0)
0 + 1 = 1 (with COUT = 0)
1 + 0 = 1 (with COUT = 0)
1 + 1 = 0 (with COUT = 1)

## Slide 11: 1-bit Binary Adder
A
+ B
S
(COUT)
0 + 0 = 0 (with COUT = 0)
0 + 1 = 1 (with COUT = 0)
1 + 0 = 1 (with COUT = 0)
1 + 1 = 0 (with COUT = 1)
Idea: chain these together to add larger numbers
2 4 8
+ 3 7 5
Recall from elementary school:

## Slide 12: 1-bit Binary Adder
A
+ B
S
(COUT)
0 + 0 = 0 (with COUT = 0)
0 + 1 = 1 (with COUT = 0)
1 + 0 = 1 (with COUT = 0)
1 + 1 = 0 (with COUT = 1)
Idea: These are chained together with a carry-in
A A A A A
B B B B B
S S S S S
CIN
COUT
(CIN)
A
+ B
S
(COUT)
0 1 1 1 0
0 1 1 0 1
1 1 0 1 1
CIN
COUT
1 1 0 0

## Slide 13: 1-bit Binary Adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A
B
CIN
COUT
S
A A A A A
B B B B B
S S S S S
CIN
COUT
A | B | CIN | COUT | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 14: 1-bit Binary Adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A A A A A
B B B B B
S S S S S
CIN
COUT
A | B | CIN | COUT | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
A’•B’•CIN
A’•B•CIN’
A•B’•CIN’
A•B•CIN
S = A’•B’•CIN + A’•B•CIN’ +
A•B’•CIN’ + A•B•CIN
Derive an expression for S

## Slide 15: 1-bit Binary Adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A A A A A
B B B B B
S S S S S
CIN
COUT
A•B’•CIN
A•B•CIN’
A’•B•CIN
A•B•CIN
A | B | CIN | COUT | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
S = A’•B’•CIN + A’•B•CIN’ + A•B’•CIN’ + A•B•CIN
COUT = A’•B•CIN + A•B’•CIN +
A•B•CIN’ + A•B•CIN
Derive an expression for COUT

## Slide 16: 1-bit Binary Adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A A A A A
B B B B B
S S S S S
CIN
COUT
COUT = A’•B•CIN + A•B’•CIN + A•B•CIN’ + A•B•CIN
A | B | CIN | COUT | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
S = A’•B’•CIN + A’•B•CIN’ + A•B’•CIN’ + A•B•CIN

## Slide 17: Apply Theorems to Simplify Expressions
The theorems of Boolean algebra can simplify expressions
  e.g., full adder’s carry-out function
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
= A’ B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= A’ B Cin + A B Cin + A B’ Cin + A B Cin’ + A B Cin
= (A’ + A) B Cin + A B’ Cin + A B Cin’ + A B Cin
= (1) B Cin + A B’ Cin + A B Cin’ + A B Cin
= B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= B Cin + A B’ Cin + A B Cin + A B Cin’ + A B Cin
= B Cin + A (B’ + B) Cin + A B Cin’ + A B Cin
= B Cin + A (1) Cin + A B Cin’ + A B Cin
= B Cin + A Cin + A B (Cin’ + Cin)
= B Cin + A Cin + A B (1)
= B Cin + A Cin + A B

## Slide 18: Apply Theorems to Simplify Expressions
The theorems of Boolean algebra can simplify expressions
  e.g., full adder’s carry-out function
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
= A’ B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= A’ B Cin + A B Cin + A B’ Cin + A B Cin’ + A B Cin
= (A’ + A) B Cin + A B’ Cin + A B Cin’ + A B Cin
= (1) B Cin + A B’ Cin + A B Cin’ + A B Cin
= B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= B Cin + A B’ Cin + A B Cin + A B Cin’ + A B Cin
= B Cin + A (B’ + B) Cin + A B Cin’ + A B Cin
= B Cin + A (1) Cin + A B Cin’ + A B Cin
= B Cin + A Cin + A B (Cin’ + Cin)
= B Cin + A Cin + A B (1)
= B Cin + A Cin + A B
adding extra terms creates new factoring opportunities

## Slide 19: A 2-bit Ripple-Carry Adder
A
Sum
Cout
Cin
B
1-Bit Adder
A0
B0
Cout
Cin
Sum0
0
A1
B1
Sum1
Cout
Cin
A2
B2
Sum2
Cout
Cin
Uses the fact that Sum = A’•B’•CIN + A’•B•CIN’ + A•B’•CIN’ + A•B•CIN
is equivalent to Sum = (A ⊕ B) ⊕ CIN

## Slide 20: Mapping Truth Tables to Logic Gates
Given a truth table:
  Write the output in a table
  Write the Boolean expression
  Minimize the Boolean expression
  Draw as gates
  Map to available gates
A B C F
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 0
1 1 1 1
F = A’BC’+A’BC+AB’C+ABC
= A’B(C’+C)+AC(B’+B)
= A’B+AC
2
3
4
5

## Slide 21: Canonical Forms
Truth table is the unique signature of a 0/1 function
The same truth table can have many gate realizations
  We’ve seen this already
  Depends on how good we are at Boolean simplification
Canonical forms
  Standard forms for a Boolean expression
  We all produce the same expression

## Slide 22: Sum-of-Products Canonical Form
AKA Disjunctive Normal Form (DNF)
AKA Minterm Expansion
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
001
011
101
110
111
A’B’C
A’BC
AB’C
ABC’
ABC
F
F= A’B’C + A’BC + AB’C + ABC’ + ABC
Read T rows off
truth table
Convert to
Boolean Algebra
Add the minterms together
1
2
3

## Slide 23: Sum-of-Products Canonical Form
Product term (or minterm)
  ANDed product of literals – input combination for which output is true
  each variable appears exactly once, true or inverted (but not both)
A B C minterms 0 0 0 A’B’C’
0 0 1 A’B’C
0 1 0 A’BC’
0 1 1 A’BC
1 0 0 AB’C’
1 0 1 AB’C
1 1 0 ABC’
1 1 1 ABC
F in canonical form: F(A, B, C) = A’B’C + A’BC + AB’C + ABC’ + ABC
canonical form  minimal form F(A, B, C) = A’B’C + A’BC + AB’C + ABC + ABC’
      = (A’B’ + A’B + AB’ + AB)C + ABC’
      = ((A’ + A)(B’ + B))C + ABC’ = C + ABC’ = ABC’ + C
= AB + C

## Slide 24: Product-of-Sums Canonical Form
AKA Conjunctive Normal Form (CNF)
AKA Maxterm Expansion
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
F
F =
Read F rows off
truth table
Negate all
bits
Multiply the maxterms together
1
2
4
Convert to
Boolean Algebra
3

## Slide 25: Product-of-Sums Canonical Form
AKA Conjunctive Normal Form (CNF)
AKA Maxterm Expansion
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
000
010
100
F
F = (A + B + C)(A + B’ + C)(A’ + B + C)
111
101
011
A + B + C
A + B’ + C
A’ + B + C
Read F rows off
truth table
Negate all
bits
Multiply the maxterms together
1
2
4
Convert to
Boolean Algebra
3

## Slide 26: Product-of-Sums: Why does this procedure work?
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Useful Facts:
We know (F’)’ = F
We know how to get a minterm expansion for F’
F’ = A’B’C’ + A’BC’ + AB’C’

## Slide 27: Product-of-Sums: Why does this procedure work?
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Useful Facts:
We know (F’)’ = F
We know how to get a minterm expansion for F’
F’ = A’B’C’ + A’BC’ + AB’C’
Taking the complement of both sides…
(F’)’ = (A’B’C’ + A’BC’ + AB’C’)’
And using DeMorgan/Comp.…
F = (A’B’C’)’ (A’BC’)’ (AB’C’)’
F = (A + B + C)(A + B’ + C)(A’ + B + C)

## Slide 28: Product-of-Sums Canonical Form
Sum term (or maxterm)
  ORed sum of literals – input combination for which output is false
  each variable appears exactly once, true or inverted (but not both)
A B C maxterms 0 0 0 A+B+C
0 0 1 A+B+C’
0 1 0 A+B’+C
0 1 1 A+B’+C’
1 0 0 A’+B+C
1 0 1 A’+B+C’
1 1 0 A’+B’+C
1 1 1 A’+B’+C’
F in canonical form: F(A, B, C) = (A + B + C) (A + B’ + C) (A’ + B + C)
canonical form  minimal form F(A, B, C) = (A + B + C) (A + B’ + C) (A’ + B + C)
      = (A + B + C) (A + B’ + C)
      (A + B + C) (A’ + B + C)
      = (A + C) (B + C)